## Slide 1: VLSI Chip Packaging Techniques
M.PRAVEEN KUMAR
R.NO.6
Notes: <number>

## Slide 2: CONTENTS
Introduction
Functions of an electronic package
Brief history of electronic packaging technology
Challenges
Electrical design, one of the driven forces on packaging technology

## Slide 3: Packaging and Packages
An electronic package is defined as that portion of an electronic structure that serves to protect an electronic element from its environment and the environment from the electronic element.
In addition to providing encapsulation for environmental protection, a package must also allow for complete testing of the packaged device and a high-yield method of assembly to the next level of integration.

## Slide 4
Functions that a package must provide
A structure to physically support the chip
A physical housing to protect the chip from the environment
An adequate means of removing heat generated by the chips or system
Electrical connections to allow signal and power access to and from the chip.

## Slide 5
Four basic requirements
Circuit support and protection
Signal distribution
Heat dissipation
Power distribution

## Slide 6: Example of a Package

## Slide 7
Signal and power distribution are accomplished through leads and wire bonds, etc.
Heat dissipation is accomplished through leads and chip support
Support and protection are accomplished through the Wiring Board/substrate, or external package, and Resin, or plastic encapsulant

## Slide 8: Functions of Packages
Protecting from the
external environment
Enabling electrical
connectivity
Heat radiation
Improving packaging

## Slide 9: First Level Interconnection
First level packaging ( or interconnection) refers to the technology required to get electrical signals into and out of a single transistor or IC; in other words, the connections required between the bonding pads on the IC and the pins of the package.

## Slide 10
This is generally accomplished by wire bonding, flip-chip bonding, or Tape-Automated Bonding.

## Slide 11
Wire Bonding
The oldest method, but is still the dominant method used today, particularly for chips with a moderate number of inputs/outputs(I/O)(~200).
This technique involves connecting gold or aluminum wires between the chip bonding pads, located around the periphery of the chip, and the contact points on the package.

## Slide 12
This process has been automated for many years, but it is still time consuming because each wire requires two bonding operations, and must be attached individually.
Other limitations of wire bonding include the requirement for minimum spacing between adjacent bonding sites to provide sufficient room for the bonding tool, the number of bonding pads that can be located around the periphery of the chip, signal delay, and crosstalk between adjacent wires.

## Slide 13
Flip-Chip Bonding
The chip is mounted upside down onto a carrier, module, or PWB. Electrical connection is made via solder bumps. The solder bumps are located over the surface of the chip in a somewhat random pattern or an array so that periphery limitation, such as that encountered in wire bonding, does not limit the I/O capability.

## Slide 15
The I/O density is primarily limited by the minimum distance between adjacent bonding pads on the chip and the amount of chip area that can be dedicated to interconnection. Additionally, the interconnect distance between chip and package is minimized since bumps can essentially be located anywhere on the chip.

## Slide 16: Second Level Interconnection
Level 2 interconnection refers to the electrical connection of an IC to a circuit board, the most common one being a conventional PWB. Following level 1 interconnection, single IC chips normally undergo encapsulation in either plastic or ceramic based packages prior to connection to a PWB.

## Slide 18: Variations of Packages
Package-to-Board attachment
Pin-Through-Hole (PTH), Surface Mount Technology (SMT)
Wire bond, Flip Chip
I/O locations
Package materials:
Plastic, Ceramic, Thin Film

## Slide 19: Package-to-Board Attachment
DIP (Dual In Line Package)
SOP (Small Outline Package)
QFP (Quad Flat Package)

## Slide 20: Peripheral Packages
Dual In Line Package
8 – 48 pins
Early 1960s (Bryant Rogers)
Small Outline Package
24 – 48 pins
Quad Flat Package
48 – 128 pins, up to 384 pins

## Slide 21
I/O requirements increased sharply.
Signal transition time between chips became a factor limiting system speed.
Signal integrity between silicon chips degraded.
Power requirements per chip increased.
A problem with heat dissipation was created.
All of these factors forced electronic packaging technology into the spotlight, resulting in a reconsideration of how ICs were being packaged

## Slide 22: 3D Stacking
Three-Dimensional Stacking:
Chips are stacked together.
One of the first commercial efforts to stack chips within a single package mated flash memory with static random-access memory (SRAM).

## Slide 23
The industry desire to reduce product size, weight, and cost while providing extra performance (shorter interconnects that lower capacitance and inductance,

## Slide 24
Contd..
reducing crosstalk, and lower power consumption) and increasing functionality, has driven 3D packaging of both chips and packages.

## Slide 25: WLP, WSP and WLS
Wafer-level packaging (WLP):
The die and package are manufactured and tested on the wafer prior to separation of the packaged devices by dicing in the flip-chip fashion.
Packages are really chip size as opposed to chip scale, which is also named as wafer-scale/chip-scale packages (WS-CSP) or wafer-level/chip-scale packaging (WL-CSP).

## Slide 26
The motivation for WLP(WSP) is that peripherally designed die can be transformed, using a thin-film technology, into a standard bump or ball footprint that is compatible with current PCB layout rules, device test practices, and assembly practice. Originally, wafer-level redistribution was intended to physically redistribute perimeter bonding pads to an area array for flip chip technology.

## Slide 27
WLP offers lowest cost per I/O, since all interconnections are formed at the wafer level at the same time, lowest testing cost since it can be done at the wafer level, lowest burn-in cost because it is done at the wafer level, elimination of under filling, and enhanced electrical performance because of the short interconnections.

## Slide 28
Wafer-level stacking (WLS)
To yield stacked die that are packaged at the wafer level.
Wafers containing ICs are interconnected using a thinly polished wafer (a few tens of microns thick) containing through-wafer vias.

## Slide 29: The Future
There appears to be little doubt that the impact of packaging on future electronic systems will continue to increase with time.
The trend will continue to be toward a more integrated approach to semiconductor packaging and system design.

## Slide 30
Consequently, the boundary between semiconductor fabrication and packaging with blur, and packaging will, by necessity, become an integral part of system design.
As packaging technology progresses, there are many problems that must be addressed.
Moisture absorption
Dielectric loss, lower loss dielectrics are critically important to higher frequency system operation

## Slide 31
For new materials, reliability issues must also be addressed.
As minimum chip geometries continue to shrink into the nanometer range, higher pin count, higher wiring density, and passive device integration will provide significant challenges to packaging technology.
If these challenges can be and are met, then thermal management will continue to provide challenges for the researcher.

## Slide 32
Thank you

## Slide 33: QUERIES….?